Calorimetry
in
High-Energy Elementary-Particle Physics
Joint Dutch-Belgian-German Graduate School
Physikzentrum Bad Honnef
8-9 September 2006
Jim Crittenden
Laboratory for Elementary-Particle Physics
Cornell University

---
Calorimetry in Action
The ZEUS
Uranium/Scintillator
Calorimeter
e + p e + quark jet + X
Deep-inelastic electron-proton scattering at HERA

---
Lecture Series Outline
Physical processes
  - Multiple scattering
  - Energy loss by electrons and positrons
    - Ionization
    - Bremsstrahlung
    - Annihilation
  - Interactions of photons
    - Photo-electric effect
    - Compton scattering
    - Pair production
  1. Energy loss mechanisms for hadrons
Electromagnetic calorimeters
  - Shower formation
  - Scintillating Crystals
  - Sampling Calorimeters
    - Sampling fraction vs photostatistics
    - Systematic limitations
Hadronic sampling calorimeters
Shower development
Leakage
Time
Energy loss mechanisms
Compensation, e/h
Role of neutrons
Linearity & Resolution
Precision limits
Calibration techniques
Test beam programs
ZEUS uranium noise method
Uniformity/intercalibration
Guided 60Co source monitoring
Laser/LED monitoring (CMS)

---
Bibliography
R. Wigmans, Energy Measurement in Particle Physics (2000)
P.B.Cushman, Electromagnetic and Hadronic Calorimeters in Instrumentation in High Energy Physics, ed. F.Sauli (1992)
C.Fabjan, Calorimetry in High-Energy Physics, in Experimental Techniques in High-Energy Physics, ed. T.Ferbel (1987)
U.Amaldi, Calorimetry in High-Energy Physics, in Experimental Techniques in High-Energy Physics, ed. T.Ferbel (1987)
R.Fernow, Introduction to Experimental Particle Physics (1986)
C. Grupen, Particle Detectors (1996)

---
General Considerations
The essential concept of calorimetry is to measure the energy of final states via total absorption. The absorption is achieved via shower formation. The precision limit is determined by the statistics inherent in this physical process, thus scaling with  where N is the number of shower particles.
A further important aspect of shower formation is the logarithmic energy scaling of the penetration depth of the shower, and attendant consequences for detector size.
These considerations lead to the following comparisons with magnetic tracking measurements:
Calorimetric energy measurements of sufficient precision are possible up to several hundred GeV. Amazing dynamic range can be achieved (ZEUS: 1/105, L3: 1/107)
Relative measurement precision scales for magnetic tracking as and for calorimetry as  Examples of crossover points are ZEUS: 20 GeV and ALEPH: 45 GeV.
Necessary detector volumes scale only logarithmically for calorimeters, in many cases making them the only feasible alternative in terms of cost/engineering effort.

---
Part I: Physical Processes
Multiple scattering
Energy loss mechanisms for electrons and positrons
  1. Ionization
  1. Bremsstrahlung
  1. Annihilation
Energy loss mechanisms for photons
  1. Photo-electric effect
  1. Compton scattering
  1. Pair production
Energy loss mechanisms for hadrons
  1. Ionization
  1. Nuclear interactions
  1. Elastic scattering (e.g. neutrons)
  1. Decays (μ, ν production)

---
Multiple Scattering
Serves our lectures as a transition from negligible perturbation of the particle trajectory to full absorption. Here we assume constant kinetic energy, i.e. elastic scattering. This process will turn out to be closely related to the transverse profile of electromagnetic showers.
Coulomb-scattering scales with the squared charges, so scattering in matter is dominated by scattering off nuclei (rather than off electrons) for Z>10. Scattering of spin 0 (Rutherford) and spin ½ (Mott) particles are identical in a small-angle approximation.
Quantum limits of range of integration over scattering angles determined by resolving atom but not nucleus. Result can be defined in terms of radiation length LR, to be defined later.
No dependence on mass of scattered particle
Example: 20 GeV muon in ZEUS uranium calorimeter
LR = 3.3 mm, x = 2.5 m ⇒ 0.7 Mb, 2x106 scatters
(ref: Fernow)

---
Energy Loss via Ionization
Bethe-Bloch Formula
(ref: PDG)
Early Fermi: 'counter-intuitive' -2
Bethe (1930): relativistic rise
Broad momentum range of
'Minimum Ionizing': 2 MeV/cm
Less loss for heavier elements

---
Bremsstrahlung
Radiation by an accelerated electron
 radiated power due to synchrotron radiation a R !
Radiation by an accelerated charge qe in the field of a charge Ze
Scales with 1/M
  - 200 times larger for e than 
Scales with Z2
  - Brems off nucleus dominates
  - Ionization scales only with Z
Scales with 1/k: 'infrared divergence'
Mean angle of photon emission
< θγ > = mec2 / E
independent of photon energy

---
Energy Loss via Bremsstrahlung
Definition of Radiation Length
Calculating the energy loss, we define rad:
Under the assumption of complete screening
of the nuclear charge by the atomic electrons,
the integral gives
Since the energy loss is proportional to the initial energy, we can define a length characterizing the exponential decrease in energy:
1/LR= 4 0 na ln(183 Z-1/3)
which is independent of the initial energy !
(ref: Fernow)
where

---
Energy Loss Mechanisms for Electrons and Positrons
in Lead
Rough Approximation: Ecritical ≅ 550 MeV / Z

---
Interactions of Photons with Matter
Photo-electric effect
  - E∝ mec2
  - ∝ Z5 !
Compton Scattering
Pair-production
  - Same physics as bremsstrahlung
LR = 9/7 Lre
NB: this is also the interaction length for photons
Low Energy:
Probability of pair-production vs Compton scattering

---
Electromagnetic Showers
Passive Material + Cloud Chamber

---
EM Calorimeter Design Parameters
(ref: Rossi,Amaldi)
Critical Energy:   550 MeV/Z
Radiation Length: X0 [g/cm2]= LR  180 A/Z2
Molière Radius: RM [g/cm2]  X0 (21 MeV/)  7 A/Z
To calculate the visible signal from the shower, define the total track length in units of X0: T.
T depends on the minimum detectable energy associated with the choice of active material: Emin
For Emin=0, all electrons and positrons are detected, and the signal T = E / , corresponding to a
sensitivity factor F = 1. Calorimetry works when F is independent of E.
To get an estimate of the signal, Rossi made two assumptions: 1) the e± deposit an energy 
in each radiation length, and 2) the bremsstrahlung and pair-production processes occur according
to their high-energy formulae. In this approximation, one obtains a reasonably accurate
parameterization for many materials of the signal:
For Emin= ,
F is about 30%.

---
Profiles of Electromagnetic Showers
Transverse
Longitudinal
Containment radius
R(95%) ≅ 2 RM
For example, a transverse cell size of
5 cm was chosen for the ZEUS uranium
calorimeter, where RM = 3 cm.
98% containment in
3 tmax + 5
For example, 20 X0 for
10 GeV electrons in copper
Electrons in Copper

---
Hadronic Shower Energy Loss
Ionization
Hadronic cascades
Electromagnetic showers (e, 0)
Neutrons with nuclear-binding energies (MeV)
Nuclear fission
Photons from nuclear de-excitation
's and's from and K decays
Many of these processes provide little or no observable signal. They represent a variety of sensitivity fractions. They also take place on a variety of time scales. The contributions vary with energy and with the types of materials used for absorber and active media.
One important consequence is that the sampling fraction for hadrons is lower than that for electrons and photons, unless one takes specific countermeasures.

---
Hadronic Showers

---
Hadron Containment
tmax = 0.2 lnE + 0.7 (E in GeV)
Homogeneous active calorimeters impractical
Note that e-6=0.2%
2 in a thousand hadrons pass through
6 interaction lengths without interacting!

---
EM Fraction of Hadron Showers
Assume 1/3 of each generation is π0's
and the number of generations increases
geometrically with the initial energy E.
Then, if the energy to produce one π0 is
E0, one may expect a scaling law:
fem = 1 - (E/E0)(k-1)
Lead
Copper
(ref: Wigmans/Gabriel)

---
Consequences of Differing Sampling Fractions
fEM and fH
Signal fluctuations are not gaussian
Fluctuations in EM part affect overall resolution
Signal is not proportional to E
Ratio of signal for electrons and hadrons depends on energy
Relative resolution does not scale with E-1/2
Purely hadronic component
 component
 Calorimeter response relative to MIPs

---
Time Development of Hadronic Showers
The energy deposition proceeds on
a variety of time scales for hadronic
showers as well, unlike electromagntic
showers.
This results in more complicated
considerations for the choices
of active media readout technology.

---
Shower Leakage
The various components of hadronic showers are contained with varying levels of success. Leakage processes which scale with the initial energy generally contribute an energy-independent term in the energy measurement resolution, reducing the effectiveness of the intrinsic statistical nature of the showers and reduce the maximum energy for which a certain level of accuracy is obtained.

---
End of Section
on
Physical Processes

---
Muons